## Slide 1: Sea Level Scenario Sketch Planning Tool
Crystal Goodison, Associate Director, GeoPlan Center
Reginald Pierre-Jean, Geospatial Developer, GeoPlan Center
Trainers and Tools: Building Coastal Flood Hazard Resiliency in Florida’s Regional Planning Councils
March 30-31, 2016

## Slide 2: Roadmap for Tools Cafe
Background & Methods
Tool Demo
Case Studies
Next Steps
Assessment for Tomorrow’s Breakout Groups

## Slide 3: 1. Background & Methods

## Slide 4: FDOT’s SLR Research
FAU’s Research Report (completed Jan 2012)
Comprehensive analysis of SLR projections, studies, models and methodologies used in Florida. Resulting recommendations:
    (1) Apply U.S. Army Corps of Engineers (USACE) methodology to develop statewide and regional projections of SLR
    (2) Develop a sketch planning tool to identify potentially vulnerable infrastructure
  UF GeoPlan Center Research
  Implement FAU recommendations
  Phase 1: Feb 2012 - Oct 2013
  Phase 2: Dec 2013 – October 2015
  Phase 3: December 2015 – April 2017

## Slide 5: Project Team
Florida Department of Transportation,
Office of Policy Planning
Maria Cahill, Project Manager
University of Florida GeoPlan Center
Crystal Goodison, Principle Investigator – Phase 2&3
Alexis Thomas, Principle Investigator – Phase 1
Russell Watkins, Ph.D, Co-PI – Phase 1
Reginald Pierre-Jean, Software Developer
Katherine Norris, GIS Analyst
Sam Palmer, GIS Analyst
Daniel Downing, Web GIS Specialist
Lance Barbour, Systems Administrator
Paul Zwick, Ph.D, Hazus modeling

## Slide 6: Mapping SLR: Data Inputs & Methods
USACE Sea Level Change Projections
Elevation Data
Chart: 
| 1992 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055 | 2060 | 2065 | 2070 | 2075 | 2080 | 2085 | 2090 | 2095 | 2100 | 2105 | 2110 | 2115 | 2120 | 2125 | 2130 | 2135 | 2140 | 2145 | 2150 | 2155 | 2160 | 2165
USACE High Rate | 0 | 0.007617 | 0.024832 | 0.047697 | 0.076212 | 0.11038 | 0.15019 | 0.19566 | 0.24677 | 0.30354 | 0.36595 | 0.43402 | 0.50773 | 0.5871 | 0.67211 | 0.76278 | 0.85909 | 0.96106 | 1.0687 | 1.1819 | 1.3009 | 1.4254 | 1.5556
USACE Intermediate Rate | 0 | 0.0068439 | 0.019334 | 0.03318 | 0.04838 | 0.064936 | 0.082846 | 0.10211 | 0.12273 | 0.14471 | 0.16804 | 0.19272 | 0.21876 | 0.24616 | 0.27491 | 0.30502 | 0.33648 | 0.36929 | 0.40346 | 0.43899 | 0.47587 | 0.5141 | 0.55369
USACE Low Rate (Current Rate) | 0 | 0.0066 | 0.0176 | 0.0286 | 0.0396 | 0.0506 | 0.0616 | 0.0726 | 0.0836 | 0.0946 | 0.1056 | 0.1166 | 0.1276 | 0.1386 | 0.1496 | 0.1606 | 0.1716 | 0.1826 | 0.1936 | 0.2046 | 0.2156 | 0.2266 | 0.2376
Tide Gauge Data & Sea Level Trends
Local trend data and water levels
Future scenarios of SLR. How fast will SLR and when? Use local data for projections
High resolution Digital Elevation Model (DEM)

## Slide 7: USACE Sea Level Change Projections
Chart: 
| 1992 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055 | 2060 | 2065 | 2070 | 2075 | 2080 | 2085 | 2090 | 2095 | 2100 | 2105 | 2110 | 2115 | 2120 | 2125 | 2130 | 2135 | 2140 | 2145 | 2150 | 2155 | 2160 | 2165
USACE High Rate | 0 | 0.007617 | 0.024832 | 0.047697 | 0.076212 | 0.11038 | 0.15019 | 0.19566 | 0.24677 | 0.30354 | 0.36595 | 0.43402 | 0.50773 | 0.5871 | 0.67211 | 0.76278 | 0.85909 | 0.96106 | 1.0687 | 1.1819 | 1.3009 | 1.4254 | 1.5556
USACE Intermediate Rate | 0 | 0.0068439 | 0.019334 | 0.03318 | 0.04838 | 0.064936 | 0.082846 | 0.10211 | 0.12273 | 0.14471 | 0.16804 | 0.19272 | 0.21876 | 0.24616 | 0.27491 | 0.30502 | 0.33648 | 0.36929 | 0.40346 | 0.43899 | 0.47587 | 0.5141 | 0.55369
USACE Low Rate (Current Rate) | 0 | 0.0066 | 0.0176 | 0.0286 | 0.0396 | 0.0506 | 0.0616 | 0.0726 | 0.0836 | 0.0946 | 0.1056 | 0.1166 | 0.1276 | 0.1386 | 0.1496 | 0.1606 | 0.1716 | 0.1826 | 0.1936 | 0.2046 | 0.2156 | 0.2266 | 0.2376
2100
5.08 ft
2060
6 – 27 in
22 in
9 in
2030
3 - 10 in

## Slide 8
Mapping SLR Scenarios
Region
+ Year
+ Projection
+ Tidal Datum
= SLR Scenario
Every decade 2040 - 2100
Based on tide gauge location
Rate of future sea level rise, eg: low, intermediate, high
Starting water level,
eg: high tide or mean sea level

## Slide 9: Subset of Old Tampa Bay area Clearwater Beach Tide Gauge 2060, High Curve, MHW 1-meter inundation
Bathtub Inundation
Inundation with Hydro-
connectivity filter
SLR Inundation
Map Layers

## Slide 10: Potentially Affected Transportation Infrastructure
GIS overlays w/ transportation layers to identify potentially at-risk facilities
Transportation facilities:
  roadways, rails, rail freight connectors, airports, sea ports
Notes: Focus on State owned facilities
Planning horizons: 2040, 2060, 2080, 2100

## Slide 11: Sea Level Scenario Sketch Planning Tool
Map Viewer
  Visualize areas of inundation and affected infrastructure
  Low technical expertise needed, no GIS software needed
GIS Data Layers
  SLR Inundation Surfaces & Affected Infrastructure layers
  GIS Software and intermediate GIS expertise needed
SLR Inundation
Surface Calculator
  Create custom inundation layers
  Intermediate/ Advanced technical/ GIS expertise needed

## Slide 12: 2.Tool Demo

## Slide 13: Tool Demo
Map Viewer
Data Download
Calculator

## Slide 14: 3. Case Studies

## Slide 15: Phase 2 Work: Testing the Tools
Hillsborough Metropolitan Planning Organization Federal Highway Administration (FHWA) Climate Change Resilience Pilot
Southeast Florida FHWA Climate Change Resilience Pilot
City of Satellite Beach Vulnerability Assessment
Monroe County Vulnerability Assessment
Sarasota County

## Slide 16: Case Studies: Testing the Tools
Hillsborough Metropolitan Planning Organization FHWA Climate Change Resilience Pilot
Used Sketch Tool map viewer, GIS data, geo-processing scripts to facilitate overlays of critical infrastructure analysis of storm surge and flooding.

## Slide 17: Case Studies: Testing the Tools
Southeast Florida FHWA Climate Change Resilience Pilot
4 County Study Area: Broward, Palm Beach, Miami-Dade, Monroe. Led by Broward MPO.
Used Sketch Tool SLR scenarios, GIS data, created custom bridge elevation data, reviewed and researched storm surge modeling.

## Slide 18: Case Studies
City of Satellite Beach
First Florida city to adopt Adaptation Action Area for Comp Plan, 2013. ECFRPC used Sketch Tool GIS data & Calculator.
Monroe County
Evaluated county transportation facilities potentially inundated under various SLR scenarios, Dr. Jason Evans, Stetson Univ.
Sarasota County
County staff used ArcMap SLR Calculator to generate scenarios & analyze critical facilities.

## Slide 19: 4. Next Steps….Changes are Coming

## Slide 20: Updated Tools in Development
Tools in Development (now – October 2016):
Web Map Viewer
  Major update/ modernization.
  Building on new platform (ArcGIS API for Javascript)
  Ability to view more decades of SLR scenarios.
SLR Calculator –new version 1.5.3
  Compatible with ArcGIS 10.3.1 and 10.4
  Increased functionality
  Can demo during breakout session (let us know if you’re interested!)

## Slide 21: Updated Data in Development
Data Enhancements (now – October 2016):
Update affected transportation layers.
MPO Regional Profiles of affected assets.
Add NOAA upper curves.
Bridge deck elevation layer.
Add storm surge & inland flooding (pilot).
Transportation facility vulnerability index (pilot).
Technical Training for MPOs:
When data & tool updates are complete, conduct trainings w/ MPO on how to use the tools (Late Fall 2016/ Spring 2017)

## Slide 22: 5. Assessment for Breakout Groups

## Slide 23: Contact: Crystal Goodison Associate Director, University of Florida GeoPlan Center goody@geoplan.ufl.edu 352-392-2351 Reginald Pierre-Jean Geospatial Developer University of Florida GeoPlan Center reginald@geoplan.ufl.edu 352-392-2351